## Slide 1: Wi-Fi Security Dangers and Protection
Prof Sharada Valiveti

## Slide 2: Introduction to Wi-Fi
Laptop (Transceiver) communicates with Access Point
Cheaper and Easy to set up the Access Point
People use hotspots at
  Cafes
  Airports
  Other locations
We refer 802.11n
Open Technology

## Slide 3: Introduction to Wi-Fi
Refers to entire family of Wi-Fi
  802.11a
  802.11b
  802.11g
  802.11n
Wireless device broadcasts its presence
  Any node within range can detect signal
  An unprotected router can be easily intruded

## Slide 4: Introduction to Wi-Fi
One type of intruder is War Driver
  Person keeps moving through the city for identifying unprotected networks
  Uses software to find unprotected networks
  Can steal information from PC or Credit Card details
  Can perform illegal activities and the owner of network may be held responsible

## Slide 5: How Wi-Fi Works?
Key component is Access Point or Router
  Contains radio transmitter
  Contains receiver
  Contains interface to a wired network
  Serves as base station
AP and all stations are called Base Station Set (BSS)

## Slide 6: How Wi-Fi Works?
Initializing the network:
  Sends probe request frames when starts
  Waits for probe response (May be multiple)
  Station selects one AP on the basis of
    Signal strength
    Error rates
  Station communicates using CSMA/CA
    RTS-CTS Mechanism
Network can have many access points and stations
  Combined together called as Extended Service Set (ESS)
Also allows users to connect directly i.e. Ad Hoc or Peer to Peer Network

## Slide 7: How Hacker invades Wi-Fi?
Hacker looks for network he wants to break in
PC automatically checks for the nearest Wireless Network and connects to it
Some networks are protected but WEP is weak and can be cracked
Hacker uses sniffers to capture data
Business data can be captured
Can use Wi-Fi as launching point of criminal activity

## Slide 8: How hotspots work?
Hotspots are generally free
Each hotspot needs its connection to internet
  Generally high-speed networks
User needs to sign up if for-pay hotspots
For-pay users cannot sign on to free hotspots