## Slide 1: Approaches in Anomaly-based Network Intrusion Detection Systems
Prof Sharada Valiveti

## Slide 2: Introduction
NIDS considers
  Packet Headers
  Payload
  Combination of Packet Headers and Payloads
NIDS considered as effective second line of defense
Types of IDS
  Signature Based Systems
    Rely on Packet Matching Techniques
  Anomaly Based Systems
    Define normal traffic and then identify deviation
    Can detect zero-day Attacks
    Require Training Program and careful setting of detection threshold
    Hence Deployment more costly

## Slide 3: Anomaly based Intrusion Detection Systems
Anomaly based NIDSs can be classified according to:
  The underlying algorithm they use
    Algorithms based on statistical models
    Algorithms based on Neural Networks
  Whether they analyze the features
    Packet oriented ABS
    Connection oriented ABS
  The kind of data they analyze
    Packet headers
    Payload

## Slide 4: Comparison of Anomaly based NIDS
System | Detection Engine | Semantic Level | Analyzed Data
iSOM | NN | PO + CO | Meta data
IntelligentIDS | NN | CO | Meta data
PHAD | S | PO | H
MADAM ID | S | CO | Meta data
SSAD | S | PO | H + P
PAYL | S | PO | P
POSEIDON | NN + S | PO | P

## Slide 5: Payload-based vs Header based Approaches
Attacks detectable by header-based systems
  Teardrop exploit (Remote Denial of Service Attack)
    Can find this attack only by looking for two specially fragmented IP datagrams, analyzing the headers
    Exploits vulnerability at network layer
  The Land Attack
    Attack sends a spoofed TCP SYN packet with same source and destination IP Address (connection initiation) and same TCP Port Source and destination
    OS goes into a loop
    Exploits vulnerability at Transport Layer

## Slide 6: Payload-based vs Header based Approaches (Contd.)
Fragmentation Defect in Tear-drop exploit

## Slide 7: Payload-based vs Header based Approaches (Contd.)
Attacks detectable by Payload – based Systems
  SQL Injection
    Listed amongst the top 10 most critical web application security vulnerabilities
    http://[target]/[postnuke_dir]/modules.php?op=modload&name=Message&files=readpmsg&start=0%20UNION%20SELECT%20pn_uname,null,pn_pass,pn_p
    Exploits vulnerability at the application layer

## Slide 8: Payload-based vs Header based Approaches
Payload Based Approaches | Header Based Approaches
Suitable to identify attacks trying to exploit vulnerabilities at the application level, where sensitive data are stored | Suitable to detect attacks directed at vulnerabilities of network and transport layer
 | Probing techniques may also be included
Attacks on application level are gaining importance and hence More useful in future | Attacks on network and transport layer are rare and hence less useful
Cannot function properly in combination with applications or application protocols which apply data encryption | Do not represent a valid solution to detect modern attacks

## Slide 9: Setting up an ABS
If distance between some function of input and model exceeds a given threshold, input is anomalous
Quality of model and value of threshold have direct influence on effectiveness of ABS
Effectiveness of NIDS is determined by its completeness and its accuracy
  Completeness =
  Accuracy =
Number of false positives per hour determines the workload of IT personnel
High FP rate is main disadvantage of ABSs

## Slide 10: Building the Model
ABS should be trained with clean data set
  Manually clean the data
    Time consuming process
    Imprecise
  Or using automatic inspection using signature based IDS
    Able to pre-process training data
    Discover well-known attacks
    Not be able to detect all attacks hence noise continues in data set
    Catching noise is never an issue
      Has a different signature when compared to attacks

## Slide 11: Building the Model
Clustering techniques can be used to obtain a good training data set
  May be used to classify training data and then disregard the data belonging to the clusters which are not dense enough to be considered significant for the training model

## Slide 12: Setting the Threshold
Low threshold high number of alarms
low false negative rate
high false positive rate
High threshold low number of alarms
high number of false negatives
low number of false positives
Optimal value depends on environment monitored and distribution of training data
Eg. Setting threshold at 3tmax / 4 yields reasonably good results (tmax is the maximum distance between analyzed data and the model observed during training phase.)

## Slide 13: PAYL and POSEIDON
IP Header + TCP Header
Payload
Destination IP (j)
Destination Port (k)
Payload Length (l)
Feature Vector
A=0,1 B=0,2 C=0,3 D=0,4
UPDATE
Mljk
PAYL Architecture
XA | XB | … | Xz
∂A | ∂B | … | ∂z

## Slide 14: PAYL and POSEIDON
PAYL Architecture
  Training Phase
  Detection Phase
  Observations
    Maximum amount of space required by PAYL is: p*l*k
      p is total number of ports monitored
      l is length of longest payload
      k is a constant representing the space required to keep the mean and the variance distribution values for each payload byte
    After comparing two neighbors, PAYL collapses similar models
    Reduction in number of model of up to a factor of 16 can be achieved
    Similar payloads could be classified in different clusters which affects negatively

## Slide 15: PAYL and POSEIDON

## Slide 16: PAYL and POSEIDON
POSEIDON Architecture
  Design goal to obtain a good, unsupervised classification
    Using SOM for Pre-processing
  Instead of using Mijk in PAYL, it uses Mnjk
Observations
  Required amount of space is p*n*k
    n indicates amount of SOM network nodes
  Allows to reduce number of models needed by a factor of 3 while achieving a better accuracy and completeness

## Slide 17: Self Organizing Maps
Topology Preserving Single Layer Maps
Suitable to analyze high dimensional data
Belongs to category of competitive learning networks
Nodes are called Neurons
  Each neuron n has a vector of weights wn associated with it
  Dimension of weights is equal to the length of longest input data
  These arrays determine SOM behavior
Phases
  Initialization
  Training
  Classification

## Slide 18: Comparison of PAYL and POSEIDON
 |  | PAYL | POSEIDON
Number of Models used |  | 4065 | `1622
HTTP | DR FP | 89,00% 0,17% | 100,00% 0,0016%
FTP | DR FP | 95,50% 1,23% | 100,00% 0,93%
Telnet | DR FP | 54,17% 4,71% | 95,12% 6,72%
SMTP | DR FP | 78,57% 3,08% | 100,00% 3,69%
Overall DR with FP < 1% |  | 58,8% (57/97) | 73,2% (71/91)
Comparison between PAYL and POSEIDON; DR stands for Detection Rate (Completeness), while FP is the false positive rate (Accuracy)

## Slide 19: Conclusions
Header – based vs. Payload – Based
Signature – based vs. Anomaly – Based

## Slide 20: Thank you!!!!
Sharada Valiveti