## Slide 1: Bio Energy

## Slide 2: Biomass
Biomass is organic matter produced by plants, both terrestrial and aquatic and their derivatives.
It includes forest crops and residues, animal manure, Agriculture waste, Municipal and Kitchen waste, discarded material from food processing plants.
Renewable source of energy
Indirect form of solar energy

## Slide 3: Biomass
Terrestrial crops include Sugar crops such as sugarcane and Sweet sorghum
Herbaceous crops, Silviculture plants such as cultured hybrid poplar, sycamore, sweet gum, Adler, eucalyptus and other hard woods.
Aquatic Crops- Grown in fresh, sea and brackish waters. Both submerged and emergent plants are considered, including sea weeds, marine algae and giant California kelp.

## Slide 4: Bio-fuels
Its conversion of biomass into more useful form by variety of techniques like digestion or fermentation, Gasification, liquefaction etc.
Fuel derived from biomass are easily handled and burnt as compared to raw biomass
Biofuels- Biogas, Fuel gas, Bio-liquids
Higher calorific values

## Slide 5: Bio-fuels
Three solid biofuels- Wood, Straw and Municipal refuse
Liquids- Methanol, Ethanol, Vegetables oil
Gases- Biogas, Methane, Fuel Gas

## Slide 6: Energy Plantation
It is methods of Tapping Maximum solar energy by growing plants
Energy farms –Ideal solar collector, virtually no maintenance, economical and non-polluting.
Photosynthesis occurring in naturally, stores more than ten times much energy annually, in plant farm than is consumed by all mankind.
In india 23% of total land area is under forests. Area under social forestry of quick growing trees has increased.
Jojaba an ever shrub around 1.7 m in height grows wild in semi-arid region of Mexico and USA. Its seeds contain 50-80 of oil.
The tree species namely Acacia, Tortilla, Albizzia, Lebbak, Prasois, Juliflora likewise have been identified adapted to hot-arid regions in our country.

## Slide 7: Biomass conversion
Direct combustion
Thermochemical conversion
  Gasification
  Liquefaction
Biochemical conversion
  Anaerobic digestion
  Fermentation

## Slide 8: Direct combustion
Direct combustion, such as wood waste and bagasse

## Slide 9: Thermochemical conversion
  Gasification
  Takes place by heating the biomass with limited oxygen to produce low heating value gas or by reacting it with steam or oxygen at high pressure and temperature to produce medium calorific value gas.
  Ex. Downdraft Gasifier, Updraft Gasifier
  Liquefaction
  Liquid yields are maximized by rapid heating of the feedstock to comparatively low temperatures. The vapors are condensed from the gas stream and these separates into a two phase: the aqueous phase (pyroligneous acid) contains a soup of water soluble organic materials like acetic acid, acetone and methanol, the non-aqueous phase consists of oils and tars. These crude product can be burnt (with some difficulty), but it is usually more profitable to upgrade to premium fuels by conventional refining techniques.

## Slide 10: Biochemical conversion
  Anaerobic digestion
  Involves the microbial digestion of biomass.
  An anaerobe is a micro-organism that can live and grow without air or oxygen, it gets its oxygen by the decomposition of matter containing it.
  Fermentation
  It is the breakdown of complex molecules in organic compound under influence of a ferment such as yeast, bactaria, etc.
  It is a well established and widely used technology for the conversion of grains and sugar crops into ethanol.

## Slide 11: Wet Process and Dry process
Wet Process
  Anaerobic digestion
  Fermentation
  Chemical reduction – It involves pressure-cooking animal wastes or plant cellulosic slurry with an alkaline catalyst in the presence of CO at temperature between 250°C to 400°C.
Dry process
  Pyrolysis – A wide range of energy rich fuels can be produced by roasting dry woody matter like straw and wood chips. Cellulose and lignin break down to simpler substance. Produce charcoal.
  Liquefaction
  Gasification

## Slide 12: Photosynthesis
The most important chemical reaction on the earth is the reaction of sunlight and green plants.
Radiant energy of sun is absorbed by the green pigment chlorophyll in the plant and is stored within the plants in the form of chemical bond energy.

## Slide 13: Biogas Generation
Introduction
Anaerobic Digestion
  Acid Formation
  Methane formation
Advantages of anaerobic digestion

## Slide 14: Factors affecting on gas Generation Rate
pH
Temperature
Total solid content of feed material
Loading rate (0.5 to 1.6 kg of volatile solid per m3)
Seeding
Uniform feeding
Diameter to depth ratio (0.66 to 1)
C to N ratio (C use for energy and N use for building the cell structure )
Nutrients (P – Night soil & N2 chopped leguminous plants )
Mixing or stirring
Retention time
Types of feedstocks
Toxicity due to end product
Pressure
Acid accumulation inside the digester (neem cake)

## Slide 15: Classification of Biogas plant
Continuous or batch types
Dome and drum type
  Floating dome type
  Fixed dome type
Different variations in drum type

## Slide 16: Floating Dome type biogas plant (KVIC Digester)

## Slide 17: Janta biogas plant

## Slide 18: Deenbandhu Biogas Plant

## Slide 19: The following data are given for a family biogas digester suitable for the output of five cows: the retention time is 20 days, temperature 30°C, dry matter consumed per day=2 kg/ Cow, biogas yield is 0.24m3/kg. The efficiency of burner is 60%, methane proportion is 0.8. Heat of combustion of Methane = 28 MJ/m3. Find: (1) the volume of biogas digester (2) the power available from the digester Assume ρm = density of dry material in the fluid = 50 kg/m3

## Slide 20: Mass of the dry input mo = 2 kg/day*5 = 10 kg/day Fluid volume Vf=mo/ρm = 10 (kg/day)/50(kg/m3) = 0.2 m3/day Digester volume Vd=Vf*tr= 0.2*20 = 4 m3 Volume of biogas Vb=biogas yield input*mass of dry input = 0.24*10 = 2.4 m3/day The Power available from the digester E=ή*Hm*Mp*Vb =0.6*28*0.8*2.4 =32.25 MJ/day=8.95 kWh/day = 370 W (continuous thermal)

## Slide 21: Calculate the volume of a fixed dome type biogas digester for the output of two cows. Also, calculate the thermal power available from biogas. Use the following data: Retention time = 30 days Dry matter produced = 2 kg/day/cow biogas yield = 0.22 m3/kg of dry matter % of dry matter in cow dung = 18% Density of slurry = 1090 kg/m3 Burner efficiency = 60% Heating value of biogas = 23 MJ/m3

## Slide 22: Dry matter produced by two cows = 2*2 = 4 kg/day A dry matter content in cow dung is only 18%, cow dung produced = 4/0.18 = 22.22 kg/day

## Slide 23: Equal quantity of water is added to make the slurry. The amount of slurry produced per day = 44.44 kg/day Slurry volume produced per day = 44.44/1090 = 0.04077 m3/day

## Slide 24: With retention time of 30 days, total slurry in digester = 30*0.04077 = 1.223 m3 As about 15% digester area is occupied by the gas, the net digester size = 1.22/0.85 = 1.44 m3

## Slide 25: Gas produced = 4*0.22 = 0.88 m3/day Thermal Energy available = 0.88*23*0.6 = 12.144 MJ/day Continuous thermal power available =140.55 W

## Slide 26: Example-3
Determine the volume of a cow dung based biogas plant required for cooking needs of a family of four adults and lighting needs with three 100 CP lamps for three hours daily. Also, Determine the required number of cows to feed the plant. Assume standard values of data where required.
Solution: Assume biogas per person = 0.227 m3/day
Biogas for lamp= 0.126 m3/hr
Assume no of cow=n
Dung produced=10 kg/day/cow, Collective cow dung=70%
Gas yield= 0.34 m3/kg of dry mass
Total Gas production