## Slide 1
Lesson 4
Resolution in Remote Sensing

## Slide 2
We have Learnt:
Definition of Remote sensing
Planck’s law of radiation
Peak emitted wavelength from sun and earth .
Electromagnetic radiation or wave
Advantages of remote sensing
Classification of Remote sensing: Based on spectral region
and based on technique
Spectral Signature of vegetation, water and soil
Panchromatic/multispectral/ Hyper
spectral remote sensing

## Slide 3: Resolution in Remote sensing
Ability to distinguish smallest feature in
remote sensing image
Human eyes? .02 mm

## Slide 4: DETECTION OF FEATURES depends: RESOLUTION
THERE ARE FOUR RESOLUTIONS IN REMOTE SNSING
Spatial resolution (what details)
Spectral resolution ( What colour and band)
Radiometric resolution ( no. of bits)
Temporal resolution ( Time interval between successive observations)

## Slide 5: Spatial resolution and coverage
Spatial resolution
  Instantaneous field-of-view (IFOV)
  Pixel: smallest unit of an image
  Pixel size
Spatial coverage
  Field of view (FOV), or
  Area of coverage or swath
In practice, objects 0.04mm wide (the width of a fine human hair) are just
distinguishable by good eyes, objects 0.02mm wide are not.
Pixel size ranges from 1.1 microns in the smallest smartphone sensor, to 8.4 microns in
a Full-Frame sensor.
B

## Slide 9
Spatial Resolution
Jensen, 2000
29 microns.
= .003 mm

## Slide 10
original image
1m pixel 2m pixel 5m pixel
10m pixel
30m pixel 
Object identification depending upon pixel size

## Slide 11: Spectral resolution (Dl ) and coverage (lmin to lmax)
Spectral resolution describes the ability of a sensor to define fine wavelength intervals
The finer the spectral resolution, the narrower the wavelength range for a particular channel or band

## Slide 14: Radiometric resolution and coverage
  Sensor’s sensitivity to the magnitude of the electromagnetic energy,
  Sensor’s ability to discriminate very slight differences in (reflected or emitted) energy,
  The finer the radiometric resolution of a sensor, the more sensitive it is to detecting small differences in energy

## Slide 15
Grayscale is a range of shades of gray without apparent color. The darkest possible shade is black, which is the total absence of transmitted or reflected light.
The lightest possible shade is white, the total transmission or reflection of light at all visible wavelength s. Intermediate shades of gray are represented by equal brightness levels of the three primary colors (red, green and blue) for transmitted light, or equal amounts of the three primary pigments (cyan, magenta and yellow) for reflected light.
Gray level resolution refers to the predictable or deterministic change in the shades or levels of gray in an image.
What is GREYSCALE/ GREYLEVEL?

## Slide 16
A healthy human eye has three types of cone cells, each of which can register about 100 different colour shades.

## Slide 17
The radiometric resolution of image data in remote sensing stands for the ability of the sensor to distinguish different grey-scale values. It is measured in bit. The more bit an image has, the more grey-scale values can be stored, and, thus, more differences in the reflection on the land surfaces can be spotted.
Range of numbers that sensor uses for recording reflected light => Quantisation level

## Slide 18: Basics of Bit
Computer store everything in 0 or 1
bits | Max. num
1 | 2
2 | 4
3 | 8
6 | 64
8 | 256
11 | 2048
12 | 4096
(2bits)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Bit no.
0
256
8 bits as an example
Resolution: 12 bits
Coverage: 0 - 4095

## Slide 21
Comparing a 2-bit image with an 8-bit image

## Slide 23: Temporal resolution and coverage
Temporal resolution is the revisit period, and is the length of time for a satellite to complete one entire orbit cycle, i.e. start and back to the exact same area at the same viewing angle. For example, Landsat needs 16 days, MODIS needs one day,.
Temporal coverage is the time period of sensor from starting to ending.

## Slide 24
Temporal Resolution
Time
July 1
July 12
July 23
August 3
11 days
16 days
July 2
July 18
August 3

## Slide 26
SUMMARY

## Slide 27: Question bank
Explain:
Spectral resolution
Spatial resolution
Radiometric resolution
Temporal Resolution